# FS4.5 KS RHOMBOS  |  Lay-on/hook-on system, hinged

| Pos............................ ..............................m² Pos............................ Pos............................ .............................running metre Pos............................ .............................running metre | Delivery and installation of durlum expanded metal panels of the FS4.5 KS RHOMBOS V1 system. A frame is butt welded onto the cut-to-size expanded metal panels. By this, precisely fitting parts are produced that are hung in a positive-locking and tension-free way into the hook-on carriers with the short sides of the welded frame of the expanded metal panels via a special substructure [see separate position]. For unhinging, disengage the panels, lower them and hang them into the hinged hooks mounted to the short sides, then fold them down. The unhinged rectangular metal panels can easily be pushed together as bundles. Tool-free dismounting is guaranteed. Tolerances and quality requirements apply according to TAIM, DIN EN 13964 and durlum standard. Material: electrolytically galvanised steel Variant: V1 (surface-welded frame) Mesh M260_1.5 Mesh length: 28 mm Mesh width: 12 mm Web width: 2.0 mm Web thickness: 1.5 mm Exp. metal thickness: approx. 3.6 mm Surface: Powder-coated similar to RAL9006-079 smooth and shiny (alternative RAL......) Layer thickness: approx. 60 µm Sound absorption: with a special durlum acoustic fleece and support Colour: black Dimension: Length ............... mm Width ............... mm € / m2 Set-up costs depending on format, design and call-off € Delivery and installation of a durlum FS4.5 KS substructure consisting of hook-on carriers U 1005 A which are mounted in longitudinal direction of the corridor. Hook-on carriers are either mounted rigidly with wall brackets U 1042 to the corridor walls or with vernier scale upper and lower parts and officially approved dowels to the corridor walls or, alternatively, using threaded rods or L-shaped primary carriers U 1040 and vernier scale upper and lower parts with officially approved dowels mounted to the bare ceiling transversely to the corridor in order to ensure a rigid suspension. The spacing of the suspension points depends on the requirements of DIN EN 13964 and the statics of the system and must be proven and established by the contractor. Ensure horizontal, flush, parallel and swing-free mounting of the U-shaped hook-on profile. Screw connections must be secured against loosening. Only constructions may be used that have been approved by the manufacturer of the expanded metal panels. All parts are made of galvanised sheet steel. €/running metre Delivery and installation of durlum perimeter trims AW 2560 to cover the joints between the rectangular metal panel and the corridor walls. The perimeter trims must be adapted on site to the joint widths and attached with dowels above the rectangular metal panels on the corridor walls. Material: galvanised sheet steel or brushed stainless steel Material thickness: according to static requirements Surface: Powder-coated similar to RAL9006-079 smooth and shiny (alternative RAL......) €/running metre |
| --- | --- |